LED CHECK

In order to check the behaviour of the photo-resistor with respect to the light intensity we used an LED point source and took measurements of resistance at varying distances from the source. There was a 1/r^2 relationship, with the fit indicating that the focal point is further back than LED source. matching a point source 7.6 cm further away than the LED itself, consistent with some focusing optics on the LED. Reproduction of the inverse-sqaure law indicates the photo-resistor’s resistance is indeed inversely proportional to the light intensity, so 1/R can be used as a measure of light intensity.

The equation of the fit was : a/(x-b)^2 +c

Final set of parameters Asymptotic Standard Error
======================= ==========================

a = 13.5443 +/- 0.3298 (2.435%)
b = -7.61403 +/- 0.2096 (2.753%)
c = 0.000718823 +/- 8.441e-05 (11.74%)

LASER WIDTH

We measured the width of the laser beam with respect to the distance from the fibre, ranging from 21.3 (cm) to roughly 2.5 (m.
The relationship between the width of the beam and the distance was linear.
The opening angle (degrees) : 1.745 +/- 0.04 (2.429%)

LASER INTENSITY

We measured the intensity of the laser beam at varying distances from the source. This was done using a photo-resistor at two different voltages 2.6V and 2V. Both were then scaled to fit on the same graph.

INTENSITY PROFILE

The laser beam was projected on a squared piece of paper 1m away from the fibre. The intensity of the projected circle was then measured using a photo-resistor. Resistance was plotted against the distance from the centre of the circle in both the +x and -x directions.

Plots of all of the above are attached below along with the data.